Data Logger Downloading

Instruction Guide

- Find PCV pipe in stream. Unscrew PCV pipe cap and take datalogger out of PCV pipe, remove black cap from data logger, and take datalogger to the laptop computer.

- One person can tighten all screws while data is exported from logger.

- Plug Optic Reader and Flashdrive into any USB laptop ports. Turn on Laptop.

- Once desktop starts up, insert data logger(levelogger) end into the optic reader.

- On desktop, double click on “Levelogger Software” icon.

- From drop down menu, select USB Serial Port COM4 (or whatever port works on your laptop) (move optic reader USB to another port if software doesn't recognize).

- Single click “Retrieve Settings From Logger” icon(2nd row, 1st button from left).

- Single click “Stop” icon to stop logger from logging

(2nd row, 5th button from left).

- Click “Yes” in the pop-up to confirm stop logging.

- Single-click “Data Control” tab (A blank table appears).

- Single-click “Download Data From Logger” icon

(the orange down arrow).

- Select “All Data” from the drop down.

- Single-click “Export Data” icon, which exports data to Excel (3rd button from left, 1st row).

- Under Save in: Select “My Documents” and double click on correct folder.

- Save file with stream name(location) and date of download (EX.: Big YC 6-27-11).

- Click Save.

- Minimize datalogger software.(minus at the top right) Double click on “Microsoft Excel” icon to open. In header, click on File, Open, select My Documents, select-view all file types, and double click on new steam data file to open.

- Double check data. While document is open, click on File, Save as, select flashdrive or passport, Save file name with location and date. Exit Excel. Maximize Datalogger program window.

- Single-click on “Levelogger Settings” tab.

- Select “Continuous Logging Mode” button

- Double check this setting:

    - Rate is set to 15 minutes.

- Single-click “Program Settings To Logger” icon (2nd rove, 2nd button from left)

- Single-click “Start Logger” icon (green play button, 2nd row, 5th from left)

***Make Sure Data Logger

Has Started Logging***

- Single-click “Yes” when asked to Erase all data

- Single-click “Yes”, then “OK” when asked to Synchronize Data Logger

- Close Levelogger Software

- Single-click “Yes” to save *.csv file to “My Documents” (file name is same as above)

- Check Battery Life on Computer. If battery life is low, charge with inverter between site locations or plug charger into electrical outlet from cigarette lighter.

- Click on “safely remove hardware” icon on bottom right corner on desktop. Take out flashdrive when “safe to remove” line pops up.

- Remove data logger and redeploy in stream. Make sure pipe cover isn't too tight when screwed back onto tube.  (Repeat for each data logger from step 4)

- Email data to Cindy Rogers at rogers944@comcast.net

- Return all equipment to PASEC room or team leader or to the team who will download next.

Troubleshooting:

    - Check that the USB ports are plugged in firmly.

    - Make sure logger is seated correctly. Take data logger out of optic reader and reinsert if needed.

    - Close and reopen data logger software.

    - Restart computer if software is not responding.

    - Let Cindy know if there were any problems during the trip.

    - Call Cindy Rogers: 724-422-1547, Call John Dudash: 724-479-8919,

Call Adam Cotchen: 814-244-3688 if all else fails.

# Text boxes

Materials needed:

Laptop		Channel lock to unscrew cap

Optic Reader	Tool to tighten bolts

Inverter		Waders, wading stick (optional)

Flash Drive		Camera (optional)

Take All Needed Equipment Listed Above      With You. When you have arrived at the         datalogger location follow these steps: